## Slide 1: Lot 3
ITS Station Management Core – Low Level Description
Michelle WETTERWALD
03/04/2012

## Slide 2: Summary
References
  Section 6.5 L221
  21/02/2012 Meeting Report
  DriveC2X WP24 – Interface IF.MGMT.2
Content
  Management High Level Schema
  Management Core detailed Schema
  Interfaces Description : GN-CM, FAC-CM, Path-MNGT, UMTS-CM, WIFI-CM
  Language used : C++
  Interfaces : Sockets UDP (address and ports in .conf files)

## Slide 3: Global Schema

## Slide 4: Detailed Schema

## Slide 5: Interface to GN-CM and G5-CM
Partner : HITACHI
This interface is based on document [3].
G5-CM is interfaced through GN-CM to avoid accessing the modem directly
Messages and types supported
    (“Event” actually means “Message”)
  Location Event
    1.0 - Update Location Event
  State Event
    4.0 Wireless State Event (used for G5-CM interface)
    4.1 Network State Event
  Configuration Event
    3.1 Get Configuration Event (Request, Reply)
    3.2 Set Configuration Event (Continuous)
    3.3 Set Configuration Event (Bulk)
Primitives Header as in [3]

## Slide 6: State Event Parameters
Wireless (per G5 channel)
  Frequency, Bandwidth
  Status, RSSI
  Data rate, Transmit Power
  Congestion level assessment
GeoNetworking
  Status
  Statistics

## Slide 7: Configuration Parameters
ITS Parameter Name | Parameter Type | DESCRIPTION / VALUES
itsStationType | 0 | 1=UEV; 30=UBR;
itsStationSubType | 1 | 0=public, 1=private
itsGnLocalAddrConfMethod | 1000 | 0=auto, 1=managed
itsGnDefaultHopLimit | 1001 | Default Hop Limit (0-255)
itsGnMaxPktLifetime | 1002 | Upper Limit of Packet Lifetime (1-6300000) [ms]
itsGnMinPktRepetitionInterval | 1003 | Lower Limit of the Packet Repetition Interval [ms]
itsGnGeoBcastForwardingAlg | 1010 | 0: Unspecified, 1: Simple, 2 Advanced (optional)
itsGnGeoUcastForwardingAlg | 1011 | 0: Unspecified, 1: Greedy, 2: ETSI-CBF, 3: Revised-CB
itsGnTrafficClassRelevance | 1020 | 0-7 [High 0 <--> 7 Low]
itsGnTrafficClassReliability | 1021 | 0-3 [High 0 <--> 3 Low]
itsGnTrafficClassLatency | 1022 | 0-3 [Low 0 <--> 3 High]
itsGnCbfMinTTS | 1030 | Minimum time-to-send [ms]
itsGnCbfMaxTTS | 1031 | Maximum time-to-send [ms]
itsGnMaxCommRange | 1040 | Theoretical radio communication range [m]
itsGnDefTxPower | 1050 | TxPower [in 1dBm steps]
itsGnDefBitrate | 1051 | Bitrate [in Mbps -- 3, 4.5, 6, 9, 12, 18, 24, 27]
itsGnDefChannel | 1052 | Channel number [176, 178, 180]
itsGnDefPriority | 1053 | Priority [0-7]
itsGnDefChannelBW | 1054 | BandWidth [MHz]
itsGnCommProfiles | 1060 | Reduced Communication Profile Table (BTP-Type, CH number)

## Slide 8: Interface to FAC-CM
Partner : ?? HITACHI ??
This interface extends document [3].
Primitives supported (“Event” actually means “Message”)
  Configuration Event
    3.1 Configuration Available Event
    3.2 Get Configuration Event (Request, Reply)
    3.3 Set Configuration Event (Continuous, Bulk)
  Profile Selection Event
    5.0 Select Profile Event (Request, Reply)
    5.1 Get Profile Event (Request, Reply)
Primitives Header as in [3]

## Slide 9: State and Configuration Parameters
Parameter Name | Parameter Type | DESCRIPTION / VALUES
ITS StationIdentifier, |  | 
Management Layer AID |  | 
supported versions of CAM and DENM |  | 
ITS Station type, |  | 
Vehicle Type, |  | 
publicVehicleType, |  | 
emergency ResponseType, |  | 
CAM btpPort |  | 
DENM btpPort |  | 
Station status, |  | 
Available exchange profile Table |  | 
Communication Profiles Table |  | 
Priorities and traffic classes Table |  | 
Current Position (set of parameters including latitude, longitude, elevation) |  | 
Speed (set of parameters) |  | 
authorizedStation |  | 
enabledInformationCentricForwarding |  | 
LDM garbageCollectionInterval |  | 

## Slide 10: Profile Events Parameters
Request
  Transaction Number
  Application Id (key to Exchange Profile Table)
  Message AID (or Flow identifier)
Reply
  Transaction Number
  Communication Profile ID

## Slide 11: Interface to Path Management
Partner : INRIA
This interface extends document [3].
Messages and types supported
    (“Event” actually means “Message”)
  State Event
    4.1 Network State Event
  Configuration Event
    3.1 Get Configuration Event (Request, Reply)
    3.2 Set Configuration Event (Continuous)
    3.3 Set Configuration Event (Bulk)
Primitives Header as in [3]

## Slide 12: State Event Parameters
UDP
  Source Ports in operation
  Destination Ports in operation
TCP
  Source Ports in operation
  Destination Ports in operation
IPv6
  Packet payload size,
  delay,
  latency,
  jitter,
  number of hops to destination

## Slide 13: Configuration Parameters (Table of paths)
Parameter Name | Parameter Key | DESCRIPTION / VALUES
Pathid |  | 
Locator |  | 
Anchor |  | 
Next hop |  | 
Group id |  | 
Path reachability |  | 
Path capabilities |  | 
Path status |  | 
Start time |  | 
End time |  | 

## Slide 14: Interface to UMTS-CM
Partner : FRANCE TELECOM
This interface extends document [3].
Messages and types supported
    (“Event” actually means “Message”)
  State Event
    4.0 Wireless State Event (used for UMTS-CM interface)
Primitives Header as in [3]

## Slide 15: State Event Parameters
3G modem
  Interface Status (Connected/Not connected),
  RSSI, BER, RSCP, ECN0,
  LTE: RSRQ, RSRP,
  MBR DL, MBR UL, PER GeoNetworking
  Status

## Slide 16: Interface to WiFi-CM
Partner : ?? FRANCE TELECOM ??
This interface extends document [3].
Messages and types supported
    (“Event” actually means “Message”)
  State Event
    4.0 Wireless State Event (used for WiFi-CM interface)
Primitives Header as in [3]

## Slide 17: State Event Parameters
WiFi Modem
  Interface Status (Connected/Not connected),
  Channel,
  Data Rate,
  RSSI,
  PER,
  Packet Transfer Delay